## Slide 1: Unlocking the potential in spate irrigation: Improved Support and Improved Governance

## Slide 2: Some basics
Area known around 2,600,000 Million
North Africa – in decline
Horn of Africa – increase for crop, livestock. agroforestry
Elsewhere in Africa – livestock related
Middle East – highly productive conjunctive systems
Iran and Pakistan – largest area, but neglected
Central Asia and Latin America – the great unknown

## Slide 3: Some more basics
People directly dependent on spate irrigation systems: 9-13 Million
Poverty pockets
Difficult and risky but can contribute substantially to food security, poverty reduction, adaptation to climate variability
Improvement options in
  Agricultural production
  Non agricultural production
  Improving livelihoods

## Slide 5
Irrigation efficiency (consumption/supply) for all irrigated areas in Saudi Arabia averaged for the period 1975 to 2005. The wheat belt with (badly managed) centre pivot irrigation systems have an efficiency of 40%. The highest efficiencies (70%) are obtained at the spate irrigation systems along the Red Sea coast!
Source: WaterWatch

## Slide 6: Case: Mochiwal Flow Division
Darabam Zam
Mochiwal Division Point
North channel:
500 ha
low lying area
West Canal:
- 3000 ha

## Slide 7: Comparing..
Perennial irrigation (dam based) | Spate irrigation
Secure supplies – provided dam has reasonable catchment and manageable sedimentation | Insecure supplies unless combined with groundwater irrigation
In shallow dams high evaporative losses, in deep reservoirs not too much | Water storage in soil profile/ shallow aquifer – low evaporation losses
Investment costs per m3 stored is high | Investment cost per m3 stored is low (if there is a fresh water aquifer)
Sedimentation may cause siltation (and prevents recharge) | Sedimentation contributes to fertility
Can store peak flows | Cannot utilize all peak flows, but shallow reservoirs may be added within command area

## Slide 8: Agricultural production - 1
New crops – biofuels, oil seeds, legumes, cucurbits, medicinal plants/ herbs
New varieties and exchange of varieties
Improved crop husbandry – seed treatment, weed control, target use of agri-inputs, etc
Market chains for main crops – capture changing market
Market chains for minor crops – mushroom, guar
Improved grain storage
Research and documentation

## Slide 9: Crop yields often vary with factor 3-5 Indicating scope for improvement of crop production with agronomic and field water management improvements

## Slide 15
Improved grain storage
Detached
from the
wall
Detached
from the floor
Opening to
take grains

## Slide 16: Agricultural production - 2
Improved soil moisture management
  Pre irrigation planting
  Promote burrowing rodents, crusteans and insects
  Improved field overflow structures
  Ploughing, mulching, field bunding
  Rules on maintaining field bunds
  Water distribution to allow second turns – keeping command area compact

## Slide 22: Non - agricultural production
Improved livestock production
  Restocking
  Paravet services
  Improved breeds (exchange)
  Range land improvement
Improved agroforestry
  Spate agroforestry
  Uprooting invasive species
  Improved marketing of non timber products
  Selective tree cutting bans

## Slide 28
Forest plantation in DI Khan (year 1)
Slope towards plants

## Slide 30: Kitara traditional production system: Documentation in Riman Village
Dripping black fluid flows on Concrete floar and is collected in a hole (traditional)
Dripping black fluid is collected through a pipe into a container with a cloth filter on top (improved traditional)

## Slide 31: Improved livelihoods
Drinking water improvements
  Improved drinking water ponds
  Sand dams
  Wells in dry rivers
  Managed artificial recharge through low weirs, subsurface dams and water spreading
  Water distribution tailored to groundwater recharge
Protection measures
  Village flood protection
  River bank protection
  Dune stabilization
  Eradication of malaria and tryposonamis

## Slide 32
LOW RECHARGE WEIR
TO SLOW DOWN AND SPREAD FLOODS

## Slide 33
Banana plantation (Yemen) failed
because of ingression of saline water
Yet overuse occurs

## Slide 36: Hand Pump Sand Filter
Filter of graded
layers of sand

## Slide 39
The downsteam apron should
be long and deep enough to withstand
the upstream formation of gullies
Important to survey channel bed
downstream and check for gullies
SOME HINTS

## Slide 41: Improved governance - 1
Wadi management at basin or subbasin level
  Upstream/ downstream use
  Maintain river morphology
  Groundwater recharge
  Flood management
  Catchment management and dune stabilization
  Biodiversity and natural vegetation (and control invasive species)

## Slide 42
Different source of income: annual fees, fines, penalties
Fee collection system is well-organized

## Slide 43: Improved governance - 2
Secure land tenure and safeguarding of water rules
  Land registration
  Codification
  Strengthen local organization for rules enforcement