| ENGINEERING STRUCTURES IN SPATE IRRIGATION Summary Overview of Options and Issues |
| --- |
| Category | Structure | Notes |
| Diversion | Weirs | Create additional head and stabilizes the river bed – but siltation in front of the weir is almost inevitable – and small earthen/ gravel/ brushwood structures are often required in the end Cut off weirs should be provided with weepholes as they may interfere with the subsurface flows |
|  | Flow dividers | Useful to keep flows in manageable proportions – need enough protection (for instance with aslar) to avoid damage |
|  | Deflection spurs | Common higher up the river/ gravel fans Catches parts of the flood – and in case of high flood can be overtopped and exclude the large flood |
|  | Gravel dykes | Suitable to divert flows towards intakes and can be alternative for permanent weirs (but need rebuilding) Reinforcement with gabions or abutments Often at angle |
|  | Soil dykes | Suitable in lowland alluvial spate systems: low cost Location and choice of material is important (silty-loamy, non-saline) Reinforcement by gabions, plastic sheets, brushwood or pegs Often build at angle |
|  | Conical abutments | Can protect intakes or heads of spurs and stabilize soil bunds |
|  | Breaching bunds | Will act as ‘fuse plugs’ and break and allow large floods to pass and save main infrastructure and command area Avoid having breaching bund high up the gravel fan as they may break too fast – proper location is in plain areas |
| Intakes | Multiple intakes (and short canals) | Preferred so as to minimize conflicts and management problems |
|  | Open intakes | Large dimension – so as to pass large volume of flood water in short time Curved wing-walls preferred |
|  | Orifice intakes | Will make it possible to exclude unwanted large floods |
|  | Gated intakes | Can allow closure of area if it Mechanical operation may be difficult and mechanical operation is expensive |
|  | Rejection spilways | Allows rejection of destructive floods |
|  | Scour sluices (preferably with curved skimming weir) | Can work but are often closed by farmers as they do not want to loose water |
|  | Sedimentation ponds | In most these do not work – as cleaning and flushing is cumbersome and farmers do not want to ‘spend’ water on this |
|  | Trash racks | Put at angle so trash is guided to main river Need provision to clean as large trash catches smaller trash |
| River bed stabilization | Bed stabilizer | Make sure weepholes are provided to allow subsurface flows to pass Masonry: steep river slopes Gabions: flat river slopes |
|  | Gabion spurs | Location and shape is important to avoid loss of area or undercutting over river bank Stepped nose to avoid scour around nose |
|  | Revetments (several materials) | Important to have strong undertoe |
|  | Vegetative bank protection | Can be natural or planted – needs protection against cutting |
| Canals and command area structures | Steep channels | Preferred in upstream areas with heavy sediment load to carry fine sediment all the way to fields (for slope look at natural drains) |
|  | Shallow wide channels | Preferred in downstream areas with soft alluvial soils to prevent uncontrolled scour |
|  | Stepped drop structures | Effective in dissipating energy In general try to avoid drop structures – can sometimes different channel route |
|  | Gabion flow division/ diversion structures | Ensure that downstream apron of gabion structure is long enough to avoid back cutting Can stabilize the bed of the flood channel |
| Field structures | Improved field intakes | Allows closure of field after it is filled with water |
|  | Overflow structures | Useful if there is level difference between to prevent uncontrolled gullying in downstream field |
| Groundwater management | Low recharge weirs | Will reduce velocity of flows and induce recharge |